## Slide 1
A
IVP 2026 // CHALLENGE #1 — USER-FIRST OR USER-FAIL?
ASIRIVE
CORTEX
Hands-free navigation for the visually impaired — one voice, no screen, cane still in hand.
HAZIQ SHAH · MUHAMMAD IRFAN NUAFAL · ERYNA NATASHA — ADMIRALTY SECONDARY SCHOOL
WITH SAVH

## Slide 2
A
// CONTENTS
WHAT'S
AHEAD
Design thinking is a loop, not a line. We followed six stages — and doubled back whenever testing proved us wrong.
01
THE CHALLENGE
user-first, and the CARE test
02
STAGE 1 — EMPATHIZE
who we design for
03
STAGE 2 — DEFINE
the problem we chose
04
STAGE 3 — MARKET RESEARCH
what exists, what misses
05
STAGE 4 — IDEATE
three design rules
06
STAGE 5 — PROTOTYPE
what we built & how it works
07
STAGE 6 — TEST
the failure that fixed it
08
REFLECTION
what comes next

## Slide 3
A
// THE CHALLENGE WE CHOSE
OUR YARDSTICK — THE CARE TEST
USER-FIRST,
NEVER USER-FAIL.
IvP 2026 Challenge #1 asks one question: does your design keep the user at the heart of everything? assistive tech has a long history of user-fail — powerful devices nobody actually uses. we held Cortex to that standard from day one.
CARE FOR THE USER
does it meet real needs, values, preferences?
ACHIEVE ITS GOAL
does it solve the problem better than what exists?
RESPECT BROADER IMPACT
is it responsible to society and cost?
ENHANCE LIVES
does daily life get genuinely better?

## Slide 4
A
STAGE 01 // DESIGN THINKING
01
02
03
04
05
06
EVERY TEST LOOPS BACK — WE ITERATE
01
EMPATHIZE
Who are we designing for — and what does getting around actually feel like for them?

## Slide 5
A
// STAGE 01 EMPATHIZE — THE SCALE
2.2 BILLION
people worldwide live with some form of vision impairment.
9 IN 10
1
■ LIVE IN LOW- AND MIDDLE-INCOME COUNTRIES
□ HIGH-INCOME COUNTRIES
Yet most assistive technology is designed — and priced — for the 1 in 10 who can pay. that mismatch is where our project begins.
SOURCES: WORLD HEALTH ORGANIZATION FACT SHEET (2023) // IAPB VISION ATLAS

## Slide 6
A
// STAGE 01 EMPATHIZE — PRIMARY RESEARCH
WE DID NOT JUST RESEARCH ONLINE.
> SESSION 01 — ONLINE INTERVIEW
daily routines & pain points
> SESSION 02 — SAVH CENTRE VISIT
guided interviews with members
> SESSION 03 — NAVIGATION WALK
we followed, they led
PRIMARY RESEARCH // SAVH — SINGAPORE ASSOCIATION OF THE VISUALLY HANDICAPPED, 2026

## Slide 7
A
// STAGE 01 EMPATHIZE — WHAT WE OBSERVED
THE DAILY TRADE-OFF
THE CANE
+Feels the ground — trusted, always ready
+Leaves hands and hearing free
−Cannot feel overhead signs or barriers
−Cannot read bus numbers or give directions
THE PHONE
+Maps, bus arrivals, information
−Stops you mid-pavement to check
−Occupies the hands and attention you need for safety
STOP-AND-CHECK
every route decision costs half a minute of stillness — a pause in the middle of a footpath. safety or knowledge: never both.

## Slide 8
A
STAGE 02 // DESIGN THINKING
01
02
03
04
05
06
EVERY TEST LOOPS BACK — WE ITERATE
02
DEFINE
After three sessions with SAVH, one problem kept surfacing. We made it ours.

## Slide 9
A
// STAGE 02 DEFINE — OUR PROBLEM STATEMENT
HOW MIGHT A VISUALLY IMPAIRED PERSON TRAVEL INDEPENDENTLY — WITHOUT PUTTING DOWN THE CANE, WITHOUT STOPPING TO CHECK A PHONE, AND WITHOUT WAITING FOR SOMEONE TO HELP?
our yardstick, agreed with users: if a solution costs hands, attention or dignity — it fails the user-first test.

## Slide 10
A
STAGE 03 // DESIGN THINKING
01
02
03
04
05
06
EVERY TEST LOOPS BACK — WE ITERATE
03
RESEARCH
What already exists — and why isn't it enough for the person holding a cane?

## Slide 11
A
// STAGE 03 MARKET RESEARCH — EXISTING SOLUTIONS
GOOD TOOLS. WRONG JOB.
PRODUCT
SNAPSHOT
WHAT IT IS
PROS
CONS — WHY IT MISSES
BE MY EYES
free app connecting users to sighted volunteers over video call
free · human judgement · handles almost any task
needs a phone in hand · depends on volunteer availability · not built for continuous navigation
ENVISION GLASSES
AI glasses (built on Google Glass) that read text and identify objects
hands-free reading · recognises objects & people
≈ US$2,500 (S$3,259 list) · reading-first, not navigation-first · screen and camera up front all day
ORCAM MYEYE
discreet clip-on camera that reads text aloud
small & discreet · strong text reading
US$2,500–4,250 · reads text — it does not guide you anywhere
SOURCES: OFFICIAL PRODUCT PAGES & PUBLISHED PRICING, 2026 // PROS AND CONS VERIFIED AGAINST USER FEEDBACK FROM SAVH SESSIONS

## Slide 12
A
// STAGE 03 MARKET RESEARCH — THE GAP
NOTHING WALKS YOU THERE.
01
COST
US$2,500+ price tags put existing assistive glasses out of reach for most families.
02
INDEPENDENCE
every alternative still needs a phone in hand, a volunteer on call — or simply stops at reading.
03
DIGNITY
keeping dignity intact: no stopping, no staring at a screen, no needing a guide everywhere you go.
the gap is navigation: genuinely hands-free, genuinely affordable, built around the journey — not around reading.

## Slide 13
A
STAGE 04 // DESIGN THINKING
01
02
03
04
05
06
EVERY TEST LOOPS BACK — WE ITERATE
04
IDEATE
What should this device be — and, just as important, what should it never be?

## Slide 14
A
// STAGE 04 IDEATE — THE DECISION
NOT A SMARTER CANE — A GUIDE FOR THE JOURNEY.
RULE 01
AUDIO-FIRST
one clear voice in the ear. eyes, hands and hearing stay exactly where they belong — on the world.
RULE 02
CANE-AWARE
the cane stays the ground sensor. we detect only what it cannot feel — head-height and beyond.
RULE 03
NAVIGATION-FIRST
directions, bus arrivals, arrival alerts — the whole journey end to end, not another reading gadget.

## Slide 15
A
STAGE 05 // DESIGN THINKING
01
02
03
04
05
06
EVERY TEST LOOPS BACK — WE ITERATE
05
PROTOTYPE
Three iterations later, here is what we actually built — and the engineering underneath it.

## Slide 16
A
// STAGE 05 PROTOTYPE — WHAT IT IS
GLASSES THAT TALK YOU THROUGH THE JOURNEY
open-ear audio — you hear Cortex and the traffic. a dual camera watches ahead; a Raspberry Pi 5 with an AI accelerator does the thinking. your phone stays in your pocket.
01
GET THERE
spoken turn-by-turn directions and bus routes
02
DON'T STOP
head-height hazards called out before you reach them
03
RIDE THE BUS
live arrival times and a wake-me-up at your stop
PROTOTYPE V3 // OPEN-EAR AUDIO · DUAL CAMERA · PI 5 + NPU

## Slide 17
A
// STAGE 05 PROTOTYPE — HOW IT THINKS
FIVE SPECIALISTS, ONE VOICE
Cortex runs five cooperating layers — four on the glasses, one in the cloud.
L0
GUARDIAN
spots hazards and warns in under 100 ms — before cloud could even wake up
L1
LEARNER
recognises places and things, from the bus stop to the kopitiam
L2
THINKER
a conversational AI brain you can just ask
L3
GUIDE
directions, bus arrivals and the route state machine
L4
MEMORY
remembers your frequently visited locations
ONE RULE: SAFETY NEVER LEAVES THE DEVICE.

## Slide 18
A
// TECHNICAL ARCHITECTURE 1 OF 3
FAST REFLEXES LOCAL, BIG BRAINS ON CALL
ON-DEVICE
REACTS < 100 MS
//YOLO vision (runs offline on the NPU)
//depth sensing + ToF laser
//safety fusion & alert engine
//navigation state machine
//offline route following
ON-DEMAND
CLOUD
//Gemini Live — the conversational brain
//Google Maps routing
//LTA bus arrival times
//memory sync to the cloud
CONNECTIVITY MONITOR — walking into an MRT underpass with no signal? safety alerts and route-following keep running on-device. the journey does not stop when the network does.

## Slide 19
A
// TECHNICAL ARCHITECTURE 2 OF 3
ONE VOICE IN. ONE VOICE OUT.
no buttons to find, no screen to unlock — talk like you would to a friend.
01
EARS
bluetooth mic + voice activity detection
→
02
UNDERSTAND
speech-to-text + the Gemini Live brain
→
03
DECIDE
intent router — 97.7% accuracy on 14 intents
→
04
ACT
tool calls: navigate, bus times, find places
→
05
SPEAK
a natural voice answers in your ear
⟲CONTINUOUS CONVERSATION — INTERRUPT ANYTIME, LIKE A HUMAN COMPANION
FALLBACK CHAIN: CARTESIA VOICE → LOCAL ENGINE — THE VOICE NEVER DIES MID-JOURNEY

## Slide 20
A
// TECHNICAL ARCHITECTURE 3 OF 3
FIVE MODES THAT SWITCH AUTOMATICALLY
IT KNOWS WHERE YOU ARE IN THE JOURNEY
a navigation engine moves through six states — so the right help arrives at the right moment, without being asked.
INACTIVE
LOADING ROUTE
NAVIGATING
WAITING FOR BUS
ON VEHICLE
ARRIVED
OUTDOOR
full hazard watch
INDOOR
cane-aware mode
BUS STOP
bus-number vision
TRANSIT
stops & interchanges
IDLE
conversation only
GPS, CAMERA AND CONTEXT DECIDE THE MODE — THE USER NEVER TOUCHES A SETTING

## Slide 21
A
// PROTOTYPE — CANE-AWARE BY DESIGN
THE CANE STAYS THE CANE. AI FILLS THE BLIND SPOTS.
HAZARD
WHITE CANE
CORTEX
WHY
GROUND-LEVEL OBSTACLES
DETECTED
STAYS QUIET
the cane already owns the ground
OVERHEAD BARRIERS & BRANCHES
MISSED
ALERT < 100 MS
the classic head-height blind spot
STAIRS GOING UP
TOO LATE
ALERT < 100 MS
spotted before the first step
FAST-APPROACHING VEHICLES
MISSED
ALERT + HAPTIC
speed measured, not guessed
indoors, Cortex stays quiet about walls and curbs the cane already handles — less noise, more trust. that single decision came straight from user testing.

## Slide 22
A
STAGE 06 // DESIGN THINKING
01
02
03
04
05
06
EVERY TEST LOOPS BACK — WE ITERATE
06
TEST
Does it work for real users — and what did we get wrong the first time?

## Slide 23
A
// STAGE 06 TEST — THE MOMENT WE LISTENED
“
THE SPATIAL AUDIO WAS OVERWHELMING — WE COULDN'T HEAR OUR SURROUNDINGS.
— SAVH USER, AFTER TESTING PROTOTYPE V1
our first version poured 3D sound effects over everything. the test said: for a blind user, your ears are a safety system — never drown them. we stripped it back to one clear voice and rebuilt around the cane. failing here is what made V2 work.

## Slide 24
A
// STAGE 06 TEST → ITERATE → REPEAT
THREE ROUNDS OF LISTENING
V1
FIRST BUILD
+spatial 3D audio everywhere
+single camera, monocular depth
+alerts for every obstacle
FAILED THE TEST — too noisy, too distracting
→
ITERATE
V2
REBUILT AROUND THE CANE
+one clear voice, cane-aware alerts
+dual camera + ToF laser depth
+navigation made the core feature
TESTED WITH SAVH — "finally, something we can live with"
→
ITERATE
V3
FIELD-READY
+outdoor & indoor auto-switching
+live bus navigation end to end
+lighter, wearable, open-ear
VALIDATED — three sessions and counting
each loop back through design thinking made the product simpler, quieter and more trusted — the opposite of what we assumed on day one.

## Slide 25
A
// REFLECTION — WHAT THE NUMBERS SAY
1/10 THE PRICE. PROVEN WITH REAL USERS.
US$186
parts cost — about 1/10 of existing AI glasses (US$2,500+)
<100 MS
local hazard reaction — faster than a blink, no network needed
97.7%
intent-routing accuracy across 14 spoken commands
3
documented SAVH user sessions shaped every major decision
COST COMPARISON: PUBLISHED PRICING OF ENVISION GLASSES / ORCAM MYEYE, 2026 // INTENT ACCURACY: INTERNAL TEST SET, 14 INTENTS

## Slide 26
A
// ROOMS FOR IMPROVEMENT
THE ROADMAP
THIS IS A
PROTOTYPE.
Cortex is a working prototype — not a finished product. it took student tools, student budgets and student hours. with the right resources, partners and time, Cortex gets better.
01
a custom single-board computer — smaller, lighter, cooler
02
longer battery life for a full school day
03
fully local navigation, no cloud needed
04
more testing with more SAVH users
SUBMISSION // 25 SEP
YOUNG INNOVATORS' FAIR // 6 NOV

## Slide 27
A
// THE WHOLE LOOP, IN ONE SENTENCE
01
02
03
04
05
06
EVERY TEST LOOPS BACK — WE ITERATE
CORTEX FILLS WHAT THE CANE CANNOT FEEL — NAVIGATION THAT IS HANDS-FREE, AFFORDABLE AND DIGNIFIED.
ASIRIVE // CORTEX
HAZIQ SHAH · MUHAMMAD IRFAN NUAFAL · ERYNA NATASHA — ADMIRALTY SECONDARY SCHOOL
ASIRIVE.COM